## Slide 1: CNC Machining Look Ahead to the Next Assignment and Next Semester
MEEG 301
Fall, 2018

## Slide 2: What is CNC Milling?
CNC = Computer Numerical Control
2-axis CNC - Computer controls the movement of the x-y table
3-axis CNC - Computer controls the movement of the x-y table and the z-axis
There are also 4- and 5- axis CNC machines. These concepts can also be applied to lathes, routers, sheet metal fabrication, etc.

## Slide 3
Manually Operated Mill
(from last semester)
2-axis CNC Mill
(x and y control)
3-axis CNC Mill
(x, y and z control)

## Slide 4: Differences between the Prototrak and Mazak mills
Trak 2-axis K3 Mill
3 HP motor
4200 RPM spindle
100 IPM rapid max
2800 lb machine weight
Manual tool changes
Mazak VCU-500C 3-axis Mill
25 HP Motor
12000 RPM spindle
1000 IPM max
18000 lb machine weight
30 Tool magazine/ automatic tool changes
Renishaw touch probe

## Slide 6: Speeds and Feeds Comparison
Trak 2-axis k3 Mill
.5” endmill 1200 rpm / 157 SFM 4 IPM feed
.25” endmill 1200 rpm /78 SFM 4 IPM feed
Mazak VCU-500C 3-axis
.5” endmill 12000 rpm /1565 SFM 120 IPM feed
.25” endmill 12000 rpm /785 SFM 84 IPM feed
3.0” facemill 6000 rpm / 4664 SFM 360 IPM feed
1.0” endmill 9500 rpm / 2505 SFM 631 IPM feed

## Slide 7: The Next Step
Introduction to CAD/CAM